## Slide 1
EPE3020 - GROUP 8
COOLING AND VENTILATION (IC) OF THE THREE-PHASE INDUCTION MOTOR

## Slide 2
  Introduction
  Overview
  Cooling means for induction motors
  Induction motors using cryogenic cooling
  Conclusion
CONTENTS:
  References

## Slide 3
INTRODUCTION
It is known that the effect of electric resistance and magnetic losses (either hysteresis or eddy currents) or the friction losses from rotation takes the form of heat losses.
All these losses decrease the efficiency and lifespan of any electric machine. Thus, several efforts were made to dissipate these heat loss.
There are various methods to cool or ventitalate a machine from self cooling fans to more complex methods using special cooling medium.

## Slide 4
  When an electric motor is in operation, the rotor and stator losses generate heat.
  Efficient cooling has a significant impact on the lifetime of motor.
  The most vulnerable components to overheating are the isolation system and the bearings.
WHY IS COOLING NEEDED?
OVERVIEW

## Slide 5
WHAT ARE THE BENEFITS OF APPROPRIATE COOLING?
  Efficient cooling has a significant impact on the lifetime of motor.
  The most vulnerable components to overheating are the isolation system and the bearings.
OVERVIEW

## Slide 6
The type of use with which the motor will be used critically defines the loading conditions as well as the rated values.
THE APPLICATION
HOW TO CHOOSE THE BEST COOLING METHOD?
OVERVIEW

## Slide 7
Not only does the motor's cooling method depend on the voltage level and the protection type (IP number), but also, the application in which the machine will be used at.
THE APPLICATION
HOW TO CHOOSE THE BEST COOLING METHOD?
OVERVIEW

## Slide 8
The mounting code (IM code according to IEC standard 60034-7) takes into account:
  The position of the motor shaft
  The type of bearing shield
  Fastening of the machine
  Method of installation
  Nature of the shaft end
WHERE THE MOTOR IS MOUNTED?
HOW TO CHOOSE THE BEST COOLING METHOD?
OVERVIEW

## Slide 9
Most industrial motors are used in well ventilated areas to provide sufficient cooling. However, some may require a higher protection against the environment (higher IP) and thus a higher IC cooling code.
OPERATING ENVIRONMENT
HOW TO CHOOSE THE BEST COOLING METHOD?
OVERVIEW

## Slide 10
IC410 - TENV - Totally Enclosed Naturally Ventilated (No fan) | 
IC611 - (formerly IC 0161) - CACA - Air-Air cooling with integral fan on motor's shaft inside stator and heat exchanger with open external circuit with fan on motor's shaft. | 
IC31W - Air-Water cooling with inlet and outlet pipe or duct for cooling water circulation. | 
Common cooling medium markings: "air" is A; "water" is W. In case, the cooling medium air mark A, it can be omitted.
Examples on cooling IC codes are:
COOLING MEANS FOR INDUCTION MOTORS

## Slide 11
INDUCTION MOTORS USING CRYOGENIC COOLING
The apparatus setup of the experiment.

## Slide 12
MACHINE CHARACTERISTICS

## Slide 13
When measuring the temperature of different parts of the rotor being immersed in LN2, it was found that all the parts did not exceed the boiling point of LN2 (i.e. 77K) but there was quite a small gradient in temperature.
TEMPERATURE MEASUREMENT
In order to measure the temperature change according to the current level during the no load test, three separae temperature sensors were use, two of which are in cotact with the rotor (Tbot and Ttop) and the other was installed in the air gap (Tgap)

## Slide 14
EXPERIMENTAL SETUP

## Slide 15
OUTPUT VALUES
Comparison between ambient temperature and cryogenic conditions (each at maximum efficiency)

## Slide 16
OUTPUT VALUES
Comparison between ambient temperature and cryogenic conditions

## Slide 17
CONCLUSION
Several efforts have been made to deal with the heat losses during machine operation. The IEC standard specifies the cooling mode, that is, the medium to be used and the type of external cooling installations (e.g., external cooling fan, water pump, etc.).
There are other cooling methods such as cooling using liquid nitrogen LN2 to circulate inside the machine parts (i.e. rotor, stator and air gap) to ensure maximum possible efficiency.

## Slide 18
REFERNCES
  Bucho, L. F., Fernandes, J. F., Biasion, M., Vaschetto, S., & Cavagnino, A. (2022, June 17). Experimental Assessment of Cryogenic Cooling Impact on Induction Motors. IEEE Transactions on Energy Conversion, pp. 1-8. doi:10.1109/TEC.2022.3183939
  Folie 1. (2017, January). Retrieved from ELIN Motoren GmbH Website: http://elinmotoren.ir/uploads/pages/files/1518958240YYRiUMz9EQV1a9nHOI968j4JCDUaGtAwopLvpXGq.pdf
  What is an IM code, and what types of electrical machines are there? (2008, December 8). Retrieved from Siemens Corporation Website: https://support.industry.siemens.com/cs/document/30320280/what-is-an-im-code-and-what-types-of-electrical-machines-are-there-?dti=0&lc=en-BO